## Slide 1: SMART PATH FOLLOWER
Using Freescale HC12 microcontroller

## Slide 2: Sections of the car

## Slide 3: Control system
PID controller
Sensor | Sensor 6 | Sensor 5 | Sensor 4 | Sensor 3 | Sensor 2 | Sensor 1 | Sensor 0
Position | 3072 | 2560 | 2048 | 1536 | 1024 | 512 | 0
Position of black line = (X)*2*ATD resolution level +(compensated reading of index(X+1) – compensated reading of index (X-1)) [if 0<X<6]
Position of black line = compensated reading of index (1) [if X=0]
Position of black line =3076- compensated reading of index (6)
ATD resolution is 256
The desired position of the black line or the setpoint is: ( position of highest index – position of lowest index)/2 = (3072 - 0)/2 = 1536
And the error = (position of center line – setpoint)

## Slide 4: PID Proportional Integral differential

## Slide 5: algorithm
The programme starts with initialization process where it initializes all its variables and macros. The a variable stop_value is created and initiated to 0 . After that the programme goes into an infinite while loop including the main body of the programme. The while loop starts with compensation of the sensor values obtained from the ATD converter. The ATD values are stored in an array out of which the sensor showing the maximum reading is slected and its index is returned . And according to the index of the sensor with highest value speed of the robot is set and the position of the car is calculated as per the formula given above. Then the error from the setpoint is calculated which is corrected by the PID control and the servo motor is given the desired duty cycle to guide the robot on its path. For convenient tuning of the car the Kp, Ki and Kd values were stored in EEPROM and it can be changed with the help switch 1 and switch 2. The PD controller was also implemented in the pulse encoder section and it helped to keep the speed of the car constant.

## Slide 6: flowchart
Start
All initialization and declaration
While(1)
Compensate Reading
B
C

## Slide 7
Servo_set
P I D
Correction
Find error
Find position
Control Speed
Find Largest
B
C

## Slide 8: Sampling time
Overall Sampling time: 0.5ms
ATD Interrupt time : Time spent in the ATD interrupt. Since this interrupt is very frequent, the time of execution of this interrupt has to as small as possible. We made it the smallest possible and the time is 0.084ms.

## Slide 9: Tools used for creation and debugging of algorithm

## Slide 10: Data logger

## Slide 11: Data Logger

## Slide 12: Virtualization Tool

## Slide 13: Codewarriors

## Slide 14: Other features
Use of floating point emulation to increase sampling time
Use of EEPROM to store the run time details

## Slide 15: THANK YOU